|  |  | DEPARTMENT OF RESOURCES | www.nt.gov.au |
| --- | --- | --- | --- |

# FILE NOTE

SUBJECT:	Sweetpea Seismic Processing – 2004 to 2006

DATE:	13/1/2011

AUTHOR:	Felicity Walker

Between 2004 and 2006, Sweetpea Petroleum (PetroHunter Energy Corporation, Falcon Oil and Gas Ltd) processed legacy seismic data and 2006 acquired seismic data in the Beetaloo Basin.  Several companies were selected to complete the processing, and minimal documentation has been received regarding the processing methodology. The table below outlines the processing flows completed, as listed in the EBCDIC headers.

# 2004 Reprocessing

Pulsonix:

# MA91-103, SH90-103

# Mig: Final Migration

Stk: Final Stack

# 2005 Reprocessing

# Kelman: MC92-102

| NEW_MIG: | ENH_STK: | ENH_MIG: |
| --- | --- | --- |
| CDP STACK | CDP STACK | CDP STACK |
| FD MIGRATION |  | KIRCHHOFF MIGRATION |
| TV GAP DECON 60MS GAP 100MSEC OERATOR | FX DECON | FX DECON |
| FILTER 0.0 6-40HZ | FILTER 0.0 6-40HZ | FILTER 0.0 6-40HZ |
| SCALE 750 MS AGC | SCALE 750 MS AGC | SCALE 750 MS AGC |

Pulsonix:

MA91-103 Southern End

| Sstk: | Smig: |
| --- | --- |
| SEGY INPUT | SEGY INPUT |
| GEOMETRY AND TRACE EDITS | GEOMETRY AND TRACE EDITS |
| REFRACTION STATICS - 500M DATUM, 4000M/SEC REP. VEL | REFRACTION STATICS - 500M DATUM, 4000M/SEC REP. VEL |
| FK FILTER | FK FILTER |
| SPIKING DECONVOLUTION - 220MS OPERATOR, 0.1% WHITE NOISE | SPIKING DECONVOLUTION - 220MS OPERATOR, 0.1% WHITE NOISE |
| SPECTRAL WHITENING - 10-70 HZ | SPECTRAL WHITENING - 10-70 HZ |
| TRACE BALANCE | TRACE BALANCE |
| VELOCITY ANALYSIS - 1 EVERY 1.6KM | VELOCITY ANALYSIS - 1 EVERY 1.6KM |
| RESIDUAL STATICS - 24MS SHIFT | RESIDUAL STATICS - 24MS SHIFT |
| TRIM STATICS - 6MS SHIFT | TRIM STATICS - 6MS SHIFT |
| DMO | DMO |
| DMO VELOCITY ANALYSIS - 1 EVERY 1.6KM | DMO VELOCITY ANALYSIS - 1 EVERY 1.6KM |
| NMO/MUTE | NMO/MUTE |
| AGC - 500MS | AGC - 500MS |
| STACK - 120 FOLD NOMINAL | STACK - 120 FOLD NOMINAL |
|  | STEEP-DIP FINITE DIFF. TIME MIG - 100% SMOOTHED STACKING VELS |
| BANDPASS FILTER - 8/12-50/60 HZ/DB | BANDPASS FILTER - 8/12-50/60 HZ/DB |
| FX DECONVOLUTION | FX DECONVOLUTION |
| FK FILTER | FK FILTER |
| AGC - 500MS | AGC - 500MS |

# 2006 Reprocessing

Pulsonix:

MA91-93, 99, 109, 200, 211, 213, 215, 217, 220, 221, 221E, 223, 223E, 225, 227, 230, 241, 251, 261, 271, 296

# MC92-63, 73, 93, 104, 104W, 202,

# MD92-225, 229

| StkA | StkB | StkC | StkD | StkE |
| --- | --- | --- | --- | --- |
| GEOMETRY AND TRACE EDITS |
| AMPLITUDE RECOVERY |
| FK FILTER |
| SPIKING DECONVOLUTION - 1 WINDOW, 220MS OP. LEN., 1.0% WL |
| TIME-VARIANT SPECTRAL WHITENING - 10-70 HZ |
| TRACE EQUALIZATION |
| REFRACTION STATICS - 500M DATUM, 4000 M/SEC REP. VEL. |
| INITIAL RESIDUAL STATICS |
| VELOCITY ANALYSIS - 1 EVERY 1200M |
| FINAL RESIDUAL STATICS |
| VELOCITY ANALYSIS - 1 EVERY 1200M |
| DMO |
| DMO VELOCITY ANALYSIS - 1 EVERY 1200M |
| NMO AND MUTE |
| TIME-VARIANT BANDPASS FILTER | BANDPASS FILTER - 8-60 HZ | TIME-VARIANT BANDPASS FILTER (TVF#7) |
| FX DECONVOLUTION |
| ENHANCEMENT FILTER |
| AGC |
|  | 2-1 TRACE COMBINE |  |  | 2-1 TRACE COMBINE |

| MigA | MigB | MigC | MigD | MigE |
| --- | --- | --- | --- | --- |
| GEOMETRY AND TRACE EDITS |
| AMPLITUDE RECOVERY |
| FK FILTER |
| SPIKING DECONVOLUTION - 1 WINDOW, 220MS OP. LEN., 1.0% WL |
| TIME-VARIANT SPECTRAL WHITENING - 10-70 HZ |
| TRACE EQUALIZATION |
| REFRACTION STATICS - 500M DATUM, 4000 M/SEC REP. VEL. |
| INITIAL RESIDUAL STATICS |
| VELOCITY ANALYSIS - 1 EVERY 1200M |
| FINAL RESIDUAL STATICS |
| VELOCITY ANALYSIS - 1 EVERY 1200M |
| DMO |
| DMO VELOCITY ANALYSIS - 1 EVERY 1200M |
| NMO AND MUTE |
| STEEP-DIP FINITE DIFFERENCE TIME MIGRATION |
| TIME-VARIANT BANDPASS FILTER | BANDPASS FILTER - 8-60 HZ | TIME-VARIANT BANDPASS FILTER (TVF#7) |
| FX DECONVOLUTION |
| ENHANCEMENT FILTER |
| AGC |
|  | 2-1 TRACE COMBINE |  |  | 2-1 TRACE COMBINE |

Sterling:

89-203

MC92-53, 61, 100, 104

ME91-90

| Stack1 | Stack1-fx | stack1-fxwht | stack1-fxwht-migr | stack1-fxwht-migrenh |
| --- | --- | --- | --- | --- |
| SEG-Y (Correlated) to Internal Format |
| Geometry /Survey Input |
| True Amplitude Gain Recovery |
| Trace by Trace Editing |
| RENEGADE Refraction/Datum/Elevation Statics Applied |
| Surface Consistent Amplitude Equalization |
| Minimum Phase Compensation |
| Surface Consistent Deconvolution 160ms Oper, |
| Spectral Whitening 8-60 Hz |
| Sort to CDP Gathers |
| (1) NMO/Mute/Surface Consistent Automatic Statics |
| (2)NMO/Mute/Surface Consistent Automatic Statics |
| RADON Multiple Attn |
| Linear Noise Attenuation |
| TV-Amplitude Equalization |
| NMO/Mute/Surface Consistent Automatic Statics |
| CDP Trim Statics |
| CDP Stack |
| Final Datum Statics |
|  | FX Decon |
|  |  | Spectral Balancing 8-80 Hz |
|  |  |  | FD Migration |
|  |  |  |  | Enhanced |

| DMOstack1 | DOMStack1-fx | DMOstack1-fxwht | DMOstack1-fxwht-migr | DMOstack1-fxwht-migrenh | DMOstack1-fxwht-migrenh2 |
| --- | --- | --- | --- | --- | --- |
| SEG-Y (Correlated) to Internal Format |
| Geometry /Survey Input |
| True Amplitude Gain Recovery |
| Trace by Trace Editing |
| RENEGADE Refraction/Datum/Elevation Statics Applied |
| Surface Consistent Amplitude Equalization |
| Minimum Phase Compensation |
| Surface Consistent Deconvolution 160ms Oper, |
| Spectral Whitening 8-60 Hz |
| Sort to CDP Gathers |
| (1) NMO/Mute/Surface Consistent Automatic Statics |
| (2)NMO/Mute/Surface Consistent Automatic Statics |
| RADON Multiple Attn |
| Linear Noise Attenuation |
| TV-Amplitude Equalization |
| NMO/Mute/Surface Consistent Automatic Statics |
| CDP Trim Statics |
| DIP MOVEOUT |
| CDP Stack |
| Final Datum Statics |
|  | FX Decon |
|  |  | Spectral Balancing 8-80 Hz |
|  |  |  | FD Migration |
|  |  |  |  | Enhanced1 | Enhanced2 |

# 2006 Processing

Pulsonix:

# SP06-01, 02, 03, 10, 11, 12, 13, 17, 18, 21, 22, 23, 24, 25, 27

| StkA | StkB | StkC | StkD | StkE |
| --- | --- | --- | --- | --- |
| GEOMETRY AND TRACE EDITS |
| AMPLITUDE RECOVERY |
| FK FILTER |
| SPIKING DECONVOLUTION - 1 WINDOW, 220MS OP. LEN., 1.0% WL |
| TIME-VARIANT SPECTRAL WHITENING - 10-70 HZ |
| TRACE EQUALIZATION |
| REFRACTION STATICS - 500M DATUM, 4000 M/SEC REP. VEL. |
| INITIAL RESIDUAL STATICS |
| VELOCITY ANALYSIS - 1 EVERY 1200M |
| FINAL RESIDUAL STATICS |
| VELOCITY ANALYSIS - 1 EVERY 1200M |
| DMO |
| DMO VELOCITY ANALYSIS - 1 EVERY 1200M |
| NMO AND MUTE |
| TIME-VARIANT BANDPASS FILTER | BANDPASS FILTER - 8-60 HZ | TIME-VARIANT BANDPASS FILTER (TVF#7) |
| FX DECONVOLUTION |
| ENHANCEMENT FILTER |
| AGC |
|  | 2-1 TRACE COMBINE |  |  | 2-1 TRACE COMBINE |

| MigA | MigB | MigC | MigD | MigE |
| --- | --- | --- | --- | --- |
| GEOMETRY AND TRACE EDITS |
| AMPLITUDE RECOVERY |
| FK FILTER |
| SPIKING DECONVOLUTION - 1 WINDOW, 220MS OP. LEN., 1.0% WL |
| TIME-VARIANT SPECTRAL WHITENING - 10-70 HZ |
| TRACE EQUALIZATION |
| REFRACTION STATICS - 500M DATUM, 4000 M/SEC REP. VEL. |
| INITIAL RESIDUAL STATICS |
| VELOCITY ANALYSIS - 1 EVERY 1200M |
| FINAL RESIDUAL STATICS |
| VELOCITY ANALYSIS - 1 EVERY 1200M |
| DMO |
| DMO VELOCITY ANALYSIS - 1 EVERY 1200M |
| NMO AND MUTE |
| STEEP-DIP FINITE DIFFERENCE TIME MIGRATION |
| TIME-VARIANT BANDPASS FILTER | BANDPASS FILTER - 8-60 HZ | TIME-VARIANT BANDPASS FILTER (TVF#7) |
| FX DECONVOLUTION |
| ENHANCEMENT FILTER |
| AGC |
|  | 2-1 TRACE COMBINE |  |  | 2-1 TRACE COMBINE |

Sterling:

# SP06-01, 02, 05, 06, 07, 08, 09, 14, 15, 16, 19, 28

| Stack1 | Stack1-fx | stack1-fxwht | stack1-fxwht-migr | stack1-fxwht-migrenh |
| --- | --- | --- | --- | --- |
| SEG-Y (Correlated) to Internal Format |
| Geometry /Survey Input |
| True Amplitude Gain Recovery |
| Trace by Trace Editing |
| RENEGADE Refraction/Datum/Elevation Statics Applied |
| Surface Consistent Amplitude Equalization |
| Minimum Phase Compensation |
| Surface Consistent Deconvolution 160ms Oper, |
| Spectral Whitening 8-60 Hz |
| Sort to CDP Gathers |
| (1) NMO/Mute/Surface Consistent Automatic Statics |
| (2)NMO/Mute/Surface Consistent Automatic Statics |
| RADON Multiple Attn |
| Linear Noise Attenuation |
| TV-Amplitude Equalization |
| NMO/Mute/Surface Consistent Automatic Statics |
| CDP Trim Statics |
| CDP Stack |
| Final Datum Statics |
|  | FX Decon |
|  |  | Spectral Balancing 8-80 Hz |
|  |  |  | FD Migration |
|  |  |  |  | Enhanced |

| DMOstack1 | DOMStack1-fx | DMOstack1-fxwht | DMOstack1-fxwht-migr | DMOstack1-fxwht-migrenh | DMOstack1-fxwht-migrenh2 |
| --- | --- | --- | --- | --- | --- |
| SEG-Y (Correlated) to Internal Format |
| Geometry /Survey Input |
| True Amplitude Gain Recovery |
| Trace by Trace Editing |
| RENEGADE Refraction/Datum/Elevation Statics Applied |
| Surface Consistent Amplitude Equalization |
| Minimum Phase Compensation |
| Surface Consistent Deconvolution 160ms Oper, |
| Spectral Whitening 8-60 Hz |
| Sort to CDP Gathers |
| (1) NMO/Mute/Surface Consistent Automatic Statics |
| (2)NMO/Mute/Surface Consistent Automatic Statics |
| RADON Multiple Attn |
| Linear Noise Attenuation |
| TV-Amplitude Equalization |
| NMO/Mute/Surface Consistent Automatic Statics |
| CDP Trim Statics |
| DIP MOVEOUT |
| CDP Stack |
| Final Datum Statics |
|  | FX Decon |
|  |  | Spectral Balancing 8-80 Hz |
|  |  |  | FD Migration |
|  |  |  |  | Enhanced1 | Enhanced2 |